## Slide 1: Supplier Reprograming Principles Coredo and WS0 Addon
Technical Hour

## Slide 2
Agenda
Supplier Reprogramming Principles (Razvan Coban)
1
Coredo Tool Description and Usage (Daniel Mindru)
2

## Slide 3
1.1. Why do we need supplier reprogramming.
After production, an ECU may be returned to Warranty Return Center for analysis in case of an issue.
The warranty colleagues can install/uninstall protections over the ECU if authorized, create dumps of the DFLASH and PFLASH and reprogram the application SW, calibration area and also flash a boot updater.
1. Supplier Reprogramming Principles

## Slide 4
1.2. Emergency Entry Concept in EMS3
- Emergency Entry is considered active if the configured precondition is fulfilled:
  DIO for Audi, Daimler
  ADC for JLR
- The Emergency Entry precondition check is done in the Boot Manager.
1. Supplier Reprogramming Principles

## Slide 5
1.2.1. The EC0 Add-on
Uses STP Command C184 – Emergency entry
1. Supplier Reprogramming Principles
COREDO
ECU
0xB8, 0x45
0xA0
0xB8, 0x00
0xA0,0xB8, 0x00

## Slide 6
1.2.2 Loading WS0 in RAM
1. Supplier Reprogramming Principles

## Slide 7
1.2.3. Authentication within the Boot Loader
Done through STP Command 181 (Authentication)
Initially, a default security level is present before authentication.
  C131 – Get ECU Info
  C150 – TSW Reset
  C181 – Authentication
If authentication is passed, the security level is upgraded and aligned with the one already present when WS0 is running :
  C131 – Get ECU Info
  C150 – TSW Reset
  C164 – Write Erase Memory
The authentication is managed through EAP interfaces (CSM / SMS).
On projects which use HSM, the authentication is performed inside the HSM.
1. Supplier Reprogramming Principles

## Slide 8
1.2.3. Authentication within the Boot Loader
The authentication is managed through EAP interfaces (CSM / SMS).
On projects which use HSM, the authentication is performed inside the HSM.
The asymetric encryption algorithm : RSA-2048
The hash function for signature: SHA-256
The RSA encryption scheme: RSAES-PKCS1-v1_5
The RSA signature scheme is RSASSA-PKCS1-v1_5
Certificate content :
  User public key
  User allowed operations
  Certificate signature
1. Supplier Reprogramming Principles

## Slide 9
1.2.3. Authentication within the Boot Loader
User Login
Download the UserCertificate
1. Supplier Reprogramming Principles
COREDO
Online Trust Center
Sends the certificate
Sends <APAR=1><N2>
Sends <APAR><N2><Signature>
Positive response if ok
Generate N2 if user has authentication rights in certificate
ECU
Hash and check with public key
N2 = 32 bytes Random number
APAR=AdministrativeParameter

## Slide 10
1.2.4. The WS0 Add-on
Supported features:
  Dump the content of the build units located in PFLASH and the NVM content (DFLASH).
  Reprogramming operations over the following build units:
    Application.
    Calibration.
    Boot Updater.
  Tuning protection operations:
    Install & uninstall flash protection (PFLASH).
    Install & uninstall host debug protection.
    Install & uninstall HSM debug protection.
  Sending of manual STP commands (e.g. dump the content of a certain address).
1. Supplier Reprogramming Principles

## Slide 11
1.2.4. The WS0 Add-on
STP Commands used within WS0:
  C131 – Get Ecu Info
  C150 – TSW Reset
  C160 – CRC & CKS Pattern
  C162 – Read Memory
  C164 – Write Erase Memory
  C180 – TUNP
  C186 – HSM Services
  C250 – Remove HSM Debug Protection
LIMAS specification available for all existing STP
commands:
1. Supplier Reprogramming Principles

## Slide 12: Repository Information
Minimum set of TSWP components to be integrated:

## Slide 13: Coredo Tool introduction
  Who needs to use a reprogramming / revival tool?
COREDO
Development phase
Project team
SW, HW, System,
Prototype team
COREDO
Production phase & serial life
Warranty return centers
Production Plants
Continental resident engineers
Packages
Acti-Diag Author
Packages
development
P HEV E SW SF PMT
Supported Use-Cases:
EMS2 + EMS3 platform Emergency Entry Dump (Dflash, Pflash) Flash ECU content Lock / Unlock Protections Send STP request

## Slide 14: Tool chain description. Test setup
Coredo
SMC
Dongle
Valid Coredo License
SmartCard
With private key for Security Access
(Only for serial ECU’s)
PC with COREDO 2.2.1 SW installation:
IT package CA0001809 (64b version&Win7) or CA0001808 (32b version&Win7)
This package install automatically SMC drivers and CardOS API
3 USB ports are required
VCI Vehicule Configuration Interface
Passthru +XS 2G
USB to CAN and/or K-line
12 V
GND
Reprogramming Cable
project specific connector
CAN_H, CAN_L, VBAT(12V), GND
USB
Power Supply
!
If EE is implemented and used, then
Emergency Entry Pin shall also be conected to GND

## Slide 15: Tool chain description
  Acti-Diag Workshop: in Continental is named COREDO and it is a tool used together with the packages developed by Acti-Diag Author for reprogramming reasons.
  User is able to:
    trace and interpret messages on CAN communication
    use direct build formats like .hex, .s19 or .mot
    dump, flash, erase ECU subsystem
    send/receive messages

## Slide 16: Coredo Tool installation
Go to SSP 7, search for Coredo and select COREDO 2.2.1.0:
For creating the SSP 7 request, follow the link details below:
  Link details
After request was solved by IT, go to Start and search for Software Portal and run it

## Slide 17: Coredo Tool installation
Select the Package „_DS CA0001809_COREDO_64bit_2.2.1.0_MUI“
Click on “Launch” button
This package will install Coredo tool on C:\LegacyApp\COREDO
Also installs drivers for SmartCard and CardOS API
Viewer
Can view information about
available KEYs on SMC

## Slide 18: Coredo Tools startup
Run Coredo from: Start-> All Programs-> Coredo:
You forgot to plug-in Coredo
dongle to activate SW license
!
USB Coredo dongle must be
connected during tool usage

## Slide 19: Package/Session description
  P HEV E SW SF PMT team will develop packages with Acti-Diag
  Packages are developed based on project specifications
  User will use these packages with together Coredo
  Packages are containing: *.apm and *.zip file
  *.apm file is used to import package in Coredo

## Slide 20: Coredo & Packages usage
At first Coredo startup, user has to navigate to the package location and select the *.apm file
Select package and click on button to Install and Run the package
Install operation: Package Data is copied to c:\LegacyApp\COREDO\Data\FlashFiles
Validate the selection to copy the package locally to Local Coredo Database on: c:\LegacyApp\COREDO\Data\Package
More packages can be imported with button or removed with button

## Slide 21: Coredo & Packages usage
If multiple sessions are already imported in Coredo Local Database, you have to select the needed one and Run or Reinstall and Run selected package
Run operation: Package Data already installed from previous Install&Run
Reinstall operation: Package Data is erased and reinstalled before running the package