## Slide 1: Vitesco Boot Concept
Go Through
11.30.2021

## Slide 2: bootloader
prepare
>This is used to reprogram ECUs App software
>General program flow

## Slide 3: Preface
This session is intentionally to introduce boot concept of HGIF (for both ECU14 and ECU17) in a higher level.
Detail can be found in attached official training material.
It will cover
  Different units such as boot manager, boot loader, end user application, and how to jump between
  Common use cases
It will not cover
  Reprogramming (for example, command, sequency, check, flash driver, …)
  Uds service
Note:
  EMS3: 3rd 32bit ECU which includes
    AutoSAR Architecture (PowerSAR),
    MultiCore
    New Boot Concept
    Basic SW (GIF, HGIF):
    Chip Set (ECU14, ECU17, …)
      ECU 14: Aurix (TC2xx), ATIC1XX,
      ECU 17: Aurix 2G (TC3xx), ATIC2XX,
Will and Will Not

## Slide 4: RunTime Units
Overview
Smallest autonomous executable entity (e.g. Boot Manager, End-User Application)
  made of one or more parts
  made of one or more sub units
  made of one or more programming units
RunTime Unit
Smallest buildable entity (e.g. RC0, 0A0)
  produces exactly one RunTime Unit part
Build Unit
Logical subdivision of a RunTime Unit (e.g. Applicative Software, Dataset, Postbuild block and Mapping Block are 4 sub units of the End-User Application)
  made of one or more programming units
Sub Unit
Programming Unit
Smallest programmable entity (also referred as slot for multi-part application)
  always shipped with prolog and epilog
  always aligned on one or more sectors
Confluence Link:
Build Units - EMR3 PSA SW - Vitesco Technologies Confluence

## Slide 5: RunTime Units
overview
RunTime Unit | Build Unit | Sub Unit | Comments
0M0 |  |  | 
 |  | LM0 | LIF， Part of 0M0
0L0 |  |  | 
 | RC0 |  | Add-On, Customer, IL0
 | XC0 |  | Add-On, Customer, IL0
 | EC0 |  | Add-On, Customer, IL0
 | WS0 |  | Add-On, Supplier, IL0
0U0 |  |  | 
 |  | 0A0 | Application SW
 |  | 0D0 | Data Set
HA0 |  |  | Added in HGIF17
HM0 |  |  | Added in HGIF17
1L0 |  |  | SBOOT, Added in HGIF17

## Slide 6: Bootloader Related tool
HW & SW
Addon | Protocol | HW | PC SW | Comments
RC0 | UDS | VECTOR HW | HEV Flash Tool or CAN Tool | Customer HW/SW tool supported
XC0 | XCP | ETAS HW | INCA/ProF | Only used in development phase
WS0 | STP | CXS （new），PHS （old） | CoReDo （from SSP7） | Used by VT’s WRC to dump, reflash
SBOOT | ??? | CoPra | ECU Test Suite (Green SW) | From BU T and now integrated to EMS3
Standalone SBOOT
  EMR3 is using this solution
  Sboot + TSW, totally independent to EMS3 Boot concept
PowerSAR SBOOT (1L0)
  A12: ongoing, will connect to Cypro Server
  GWM: not planned

## Slide 7: EMR3: Boot flow
flow

## Slide 8: Emergency Entry
Introduction
What is the Emergency Entry function?
  One Way to enter to the Supplier Reprogramming Session mode
    Required for Extended Supplier diagnostics (e.g warranty return -> WS0)
    Typically required to update the Boot Loader
  Can be applied also in case of damaged Boot Updater, if Boot Loader plus EC0 addon still present in the ECU
Emergency Entry does not compromise Security
Emergency Entry is NOT related to Safety
Boot Manager is offering two different ways of using EEntry:
  Pin detection based,
  Communication message based (only CAN is supported)

## Slide 9: Emergency Entry
EMS3 Boot Flow complete
EEntry validation is
mandatory to reach
this state (EC0 or 1L0)

## Slide 10: EMR3 boot concept
Lifecycle example

## Slide 11: Any questions?