## Slide 1: COREMA T1 13.x.x Automation result
log checking
Timisoara, 12.04.2021
Ovidiu Tripon

## Slide 2: COREMA T1 – EXPERT – Step 11
Step 11 : Can Configuration
CAN settings are already prefilled :
  CanPcToEcuId = T1 Host Tx ID (should be the same as T1 Target Rx ID)
  CanEcuToPcId = T1 Target Tx ID (should be the same as T1 Host Rx ID)
CSV report is also generated with prefilled settings.
  Target Rx ID=GUI TxID
  Target TxID = GUI RxID
  Default CAN IDs
  Customer related CAN IDs

## Slide 3: COREMA T1 – Runtime Measurements Plausibility Check
Failed commands
  These are marked with “Warning”
  These functions were not measured, so you should analyze:
    The warning message
    The functions for which a certain warning had been displayed

## Slide 4: COREMA T1 – Runtime Measurements Plausibility Check
Failed commands, functions not measured, and the common reasons are
    Functions is not called by the Application
    The symbol is not a function but a Macro so it doesn’t have a Start/End address ( needed by the Flex measurement)
In these cases, the Flex warnings are like this :
  Warning: "FlexSWF – Symbol name " failed: focus measurement did not get valid results: element was not executed
  Warning: "FlexSWF - Symbol name " failed: target state: DATA_READY focus measurement did not get valid results: element was not executed
  Warning: Focus measurement for element Symbol name was successful but there is at least one missing T1.cont
  the important statement is “Element was not executed”
Its quite common to have warnings like these as not all of the automatically determined functions by CoremaT1 ( based on the project’s tree) are also called by the application.

## Slide 5: COREMA T1 – Runtime Measurements Plausibility Check
Failed commands, functions not measured, other errors :
  CAN communication between the Target code ( ECU) and the Host Software (T1 GUI) is not working
    This is mainly caused by WRONG connection of the T1 Dongle CAN wires to the right ECU CAN bus (e.g. if CCP node is used for T1 messages, the dongle should be connected to this CAN bus not to another one)
  In this case
    make sure the SW is running without resets
    ask for project test bench support to get the right CAN bus
    just plug the T1 Dongle CAN cables on other CAN bus and try again until you have communication (with respect to CAN-H / CAN-L wires)

## Slide 6: COREMA T1 – Runtime Measurements Plausibility Check
Failed commands, functions not measured, other errors :
  In some situations, if the selected CAN bus for T1 messages is quite busy then it could be that the T1 GUI enters in a timeout mode and the measurements results for certain functions are lost
In these cases, the Flex warnings from the log file are like this :
  Warning: "FlexSWF - Symbol name " failed: focus measurement did not get valid results: focus state invalid”
  the important statement is “Focus state invalid” in this case
If there are a high number of warning messages like this then we have 2 options:
  Change the T1 HOST timeouts for CAN frames
  Select another active CAN node on which the Bus load is not that high
  Use the same CAN node but change the T1 CAN IDs to increase the priority

## Slide 7: COREMA T1 – Runtime Measurements Plausibility Check
Summary :
  Flex warnings like Element was not executed are quite common for a reduced number of functions. The project can analyze the functions which are not called to see if the measurement conditions are the right ones.
  Flex warnings like Focus state invalid are more severe and mainly indicates that the measurement was not performed for that functions. These should be analyzed because missing measurements for called function will influence the CPU load calculation
  Flex error Enable Link means the CAN communication cannot be established because the SW is not running, T1 dongle is not plugged to the correct CAN Bus.
For other details please refer to the T1.Help file present on the WIKI page

## Slide 8: Let’s discuss!