## Slide 1: Analog to Digital Converter (ADC ) Driver Training Slides
ECU 17
www.continental-corporation.com
Harald Paschke
Driver Responsible
P E&DS SE EEA BSW RBG1
Harald.Paschke@continental-corporation.com
+49 941 790 928747
Jithin Jose
Driver Developer
P E&DS SE EEA BSW BLR
Jithin.Jose@continental-corporation.com
+91-80-66791100-3152

## Slide 2
Agenda
Functional Description & Features
1
APIs
2
Integration Highlights
3
Configuration
4
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
HW Resources
6
Constraints & Limitations
7

## Slide 3: ADC Driver Functional Description & Features

## Slide 4: ADC Driver Functional Description & Features
Versatile ADC
Successive Approximation
Low Latency-time
High Accuracy
Easy to use
Delta Sigma ADC
High resolution
High stability
  Filters and noise reduction
Fast Comapre
Successive Approximation
High Speed (5 Msampes/s)
Dedicated compare features
VADC
DSADC
FCOMP
ADC
Driver

## Slide 5: ADC Driver Functional Description & Features
VADC: Versatile ADC
- Primary
- Secundary
FCOMP: Fast Compare
DSADC: Delta Sigma ADC
ADC Driver

## Slide 6: ADC Driver Functional Description & Features
The ADC driver provides:
  AUTOSAR APIs (adc.h)
  PowerSAR APIs (iopt_adc.h)
  Two (CESSAR) user configuration for VADC + FCOMP and DSADC
4 Trigger trigger modes for VADC / 1 trigger mode for DSADC
Support of external Buffers (linear and circular)
Result Handling (VADC)
  Internal: Internal setup of DMA, copy results from result register to the buffer (internal or external)
  External: The user takes care to fetching the results from the ADC peripheral on his own
Notification:
  The user can set up a notification which is called after the configured set of conversions

## Slide 7: ADC Driver - VADC Functional Description & Features
Up to 11 HwUnits ## 3 Conversion Groups + 1 Master Sync Group ## 8/16 Channels
Each HwUnit has one Analog to Digital Converter ( Successive Approcimation [SAR] )
Conversion groups (Queues) get activated/started via trigger signals
An arbiter resolves concurrent conversion requests
VADC (internal structure)
HwUnit y
. . . .
HwUnit 1

## Slide 8: ADC Driver Functional Description & Features
Hardware Unit 0 / Converter 0
Channel 0
Channel 1
Channel 2
Channel 8/16
.
.
.
Conversion Group 0
Conversion Group 1
Conversion Group 2
Request Arbiter
Sync Request
External Request(s)
Analog Converter
Timer Unit(s)
Master Sync Group

## Slide 9: ADC Driver - VADC Functional Description & Features
Periodic software trigger (e.g.10ms )
    10ms: convert
    20ms: fetch result (10ms), convert
    30ms: fetch result (20ms), convert
    n ms: fetch result (n-10ms), convert
External Multiplexer (EMUX) support
    1:8 multiplexer
    Internal result handling (in software)
AutoScan
1
Triggert via function call
Internal result Handling:
    via interrupt after group convertion
SwTrigger
2
Adc_StartGroupConverion(ConversionGroup)
4 trigger types per conversion group (Queue)

## Slide 10: ADC Driver - VADC Functional Description & Features
Same features as HwTrigger
    Triggered via hardware signal
    Internal/External result handling
    Single or continuous mode
Synchronized conversion of multiple groups
One master triggers up to three slaves
    Special connection between certain HwUnits
Triggered via hardware signal
    e.g. Falling edge on input-pin or TOM
Resulte handling:
    Internal (internal DMA configuration)
    External (no DMA configuration)
    Linear or circular buffer (streaming)
  Convertion modes
    Single: Only convert once
    Continous: Always convert on trig. sig.
HwTrigger
3
SyncTrigger
4

## Slide 11: ADC Driver - VADC Functional Description & Features
3 Request Sources (Trigger Type) can be assigned to 3 Conversion Groups (Queues)
Only HwTrigger and the Master Sync Group (Queue) are connected to a hardware line
SwTrigger and Autoscan are handled completely in software ( iopt_adc function calls )
Priorities (CESSAR):
  High (Q0) : HwTrigger
  Medium (Q1): SwTrigger
  Low (Q2): AutoScan
  Highest (byHw): MasterSync

## Slide 12: ADC Driver Functional Description & Features
Hardware Unit 0 (Primary TC38x)
Channel 0
Channel 1
Channel 2
HwTrigger
SwTrigger
Autoscan
Request Arbiter
Sync Request
External Request(s)
Analog (SAR) Converter
Timer Unit(s)
Channel 3
Channel 4
Channel 5
Channel 6
Channel 7
Q0
Q1
Q2
Master Sync Group

## Slide 13: ADC Driver - VADC Functional Description & Features
Linear streaming buffer (external)
Example
  Length: 15
  Channels: 3
Buffer will be reset again via
  VadcEnableHwTrigger(Group)

## Slide 14: ADC Driver - VADC Functional Description & Features
Circular streaming buffer (external)
Example
  Buffer length: 15
  Channels: 3

## Slide 15: ADC Driver - VADC Functional Description & Features
Synchronized conversion
  CH0,1,2,4,5: regular conversion (e.g. HwTrigger, AutoScan)
  CH3: Used for parallel conversion
  Internal trigger / synchronisation signal
Master:
Slave 1:
Slave 2:
Master:
Slave 1:
Slave 2:
Slave 2:

## Slide 16: ADC Driver - VADC Functional Description & Features
Data Reduction
  Used for digital anti-aliasing filtering
  automatically adds up to 16 conversions before issuing a valid result
+
+
+
+
+
+

## Slide 17: ADC Driver - VADC Functional Description & Features
Fast Compare
  Up to 8 independent channels (no arbitration)
  Conversion result gets compared to a configurable reverence band
The output can be routed e.g. to a output pin or a user provided function

## Slide 18: ADC Driver - VADC Functional Description & Features
Bandgap Voltage Measurement
  Measuring of the bandgap voltage provided by the Power Management Subsystem (PMS).
  Used for Module integrity test (ECM3)
  Implemented via SwTrigger only
    Internal Routing to channel 0 and channel 1 (via alias feature)

## Slide 19: ADC Driver - VADC Functional Description & Features
Broken Wire Detection (BWD)
  Test for proper connectivity
    Discharge / Charege the converter network before sampling the new input channel
    Reflection of a reduced result value if the input signal is no more conneted
  Based on the measured voltage the user can decide necessary actions for broken wire detection.

## Slide 20
The first step in a delta - sigma measurement is a delta modulation. In delta modulation the change in the signals (it´s delta) is encoded, rather than the absolute value.
The converters provide a lot of filters. Usually the settings are provided by HW team.
ADC Driver - DSADC What is a delta sigma ADC

## Slide 21
DSADC supports following conversion:
  Streaming trigger
Possibility to configure different filters for removing results that are beyond range.
  Main filter using finite impulse response - FIR filter.
  Main filter using cascaded integrator - comb filter - CIC filter.
  Auxiliary filter.
DSADC needs to be calibrated during initialization phase and during runtime.
(e.g. due to higher change of the temperature)
The DSADC is much faster than the VADC.
Once a converter is activated / started the conversion is always running.
Each converter channel operates independent to the others.
On chip modulators accept signals for single ended, differential ended or pseudo differential ended modes.
ADC Driver - DSADC Functional Description & Features

## Slide 22
Agenda
Functional Description & Features
1
APIs
2
Integration Highlights
3
Configuration
4
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
HW Resources
6
Constraints & Limitations
7

## Slide 23: ADC Driver - VADC APIs
ADC_GETVERSION_IF | 
Adc_GetVersionInfo | Returns the version information of this module.
AR_ADC_IF | 
Adc_Init | This interface is used for ADC Initialization.
Adc_DeInit | This interface is used for ADC shutdown.
Adc_SetupResultBuffer | This interface is used to setup the result buffer.
Adc_GetStreamLastPointer | Returns the location in the ADC result buffer to the oldest conversion result not yet read.
Adc_EnableGroupNotification | Enables the notification mechanism for the requested ADC group.
Adc_DisableGroupNotification | Disables the notification mechanism for the requested ADC group.
Adc_StartGroupConversion | Starts the conversion of all channels of the requested ADC group.
Adc_EnableHardwareTrigger | Enables the hardware trigger for the requested ADC Channel group.
Adc_DisableHardwareTrigger | Disables the hardware trigger for the requested ADC Channel group.
Adc_ReadGroup | Returns the result values of requested group channels after conversion.

## Slide 24: ADC Driver - VADC APIs
IOPT_ADC_AUTOSCAN_IF | 
Iopt_Adc_ActivateAutoscanTrigger | Starts the conversion for all configured Autoscan groups.
IOPT_ADC_BANDGAP_IF | 
Iopt_Adc_GetBandGapValues | Provides theoretical bandgap voltage along with UpperBoundaryVoltage and LowerBoundaryVoltage
IOPT_ADC_CONTROL_IF | 
Iopt_Adc_Init | Initializes the ADC peripheral.
Iopt_Adc_Shutdown | Stops all ADC driver activity on all configured HwUnits, resets all ADC HwUnits.
Iopt_Adc_GetGroupStatus | Returns the status of conversion for the requested group.
Iopt_Adc_GetResult | Reads the result of the latest ADC conversion for the requested channel.
Iopt_Adc_ReadGroup | Reads the latest available conversion results of the requested group.
IOPT_ADC_HWTRIGGER_IF | 
Iopt_Adc_EnableHardwareTrigger | Enables the Hardware Trigger signal for the given ADC group.
Iopt_Adc_DisableHardwareTrigger | Disables the Hardware Trigger signal for the given ADC group.
Iopt_Adc_GetStreamLastPointer | Returns two values, number of valid samples stored in the result buffer, the pointer to latest result.
Iopt_Adc_SetupResultBuffer | Prepares the external result buffer of a streaming type Hardware Trigger.

## Slide 25: ADC Driver - VADC APIs
IOPT_ADC_SYNC_IF | 
Iopt_Adc_SetSyncBuffer | Prepares the user defined result buffer for synchronized conversion.
Iopt_Adc_StopSyncBuffer | Stops the running synchronized conversion and resets the used resources.
Iopt_Adc_SyncGetStreamLastPointer | Returns two values, number of valid samples stored in the result buffer and the pointer to latest results.
IOPT_ADC_SIGNAL_IF | 
Iopt_Adc_EnableGroupNotification | Enables the notification mechanism for the requested ADC channel group.
Iopt_Adc_DisableGroupNotification | Disables the notification mechanism for the requested ADC channel group.
IOPT_ADC_SIGNAL_IF | 
Iopt_Adc_StartGroupConversion | Starts conversion of all channels of the requested ADC group.

## Slide 26: ADC Driver - DSADC APIs
IOPT_ADC_DS_FILTER_IF | 
Iopt_Adc_DsEnableFilter | Enables or disables different configuration parameters of main or comb filter.
IOPT_ADC_DS_GAIN_IF | 
Iopt_Adc_DsSetGain | This operation sets the gain factor of a DSADC channel.
IOPT_ADC_DS_MAIN_IF | 
Iopt_Adc_DsInit | Initializes all the configured features of DSADC and also the Filter configuration.
Iopt_Adc_DsShutdown | Stops all converters and resets all registers and data variables.
Iopt_Adc_DsGetStreamLastPointer | Returns two values, number of valid samples stored in the result buffer and the pointer to latest results.
Iopt_Adc_DsSetUpResultBuffer | Prepares the external result buffer where the conversion results will be stored.
Iopt_Adc_DsDisableHardwareTrigger | Disables the DSADC module to store result data inside the external user buffer.
Iopt_Adc_DsEnableHardwareTrigger | Enables the DSADC module to store result data inside the external user buffer.
Iopt_Adc_DsEnableGroupNotification | Enables or disables the activation of the notification at a completed group conversions.
Iopt_Adc_DsCalibrateDevice | Calibrates the DSADC converter due to change in the temperature or other conditions.
Iopt_Adc_DsGetCalibStatus | Returns the calibration status of the converter.
Iopt_Adc_DsActivateDevice | Activates or deactivates a particular converter.

## Slide 27: ADC Driver APIs (PowerSAR)
Iopt_Adc_ActivateAutoscanTrigger
  This interface starts the conversion for all configured autoscan groups.
Iopt_Adc_GetBandGapValues
This interface provides theoretical bandgap voltage along with UpperBoundaryVoltage and LowerBoundaryVoltage.
Iopt_Adc_GetGroupStatus
  This operation returns the status of conversion for the requested group.
  1 - Conversion of the group is completed
  0 - Conversion of the group is either not requested or not completed
Iopt_Adc_GetResult
  This operation is used to read the result of the latest ADC conversion for the requested channel. This interface can be used for autoscan group, software trigger group or hardware trigger group with the internal result buffer. The result value is left shifted by 3 bits to get a 15 bit alignment.
Iopt_Adc_ReadGroup
  The function Adc_ReadGroup read the latest available conversion results of the requested group. Reads the group conversion result of the last completed conversion round of the requested group and stores the channel values starting at the DataBufferPtr address.

## Slide 28: ADC Driver APIs (PowerSAR)
Iopt_Adc_EnableHardwareTrigger
  This interface enables the hardware trigger signal for the given ADC group. This operation prepares the ADC converter and related variables to start hardware trigger based conversion.
Iopt_Adc_DisableHardwareTrigger
  This interface disables the hardware trigger signal for a given ADC group. It also stops the ongoing conversion of the given ADC group.
Iopt_Adc_GetStreamLastPointer
  This interface returns two values, number of valid samples stored in the result buffer, the pointer to latest result.
Iopt_Adc_SetupResultBuffer
  This operation prepares the external result buffer of a streaming type hardware trigger.
Iopt_Adc_EnableGroupNotification
  This interface enables the notification mechanism for the requested ADC channel group. This interface has to be called before starting the ADC group conversions.

## Slide 29: ADC Driver APIs (PowerSAR)
Iopt_Adc_DisableGroupNotification
  This interface disables the notification mechanism for the requested ADC channel group.
Iopt_Adc_StartGroupConversion
  This interface starts conversion of all channels of the requested ADC group. Software trigger based conversion results are stored in the internal result buffer which can be accessed by calling the interface GetResult.
Iopt_Adc_SetSyncBuffer
  This operation is used to setup the user defined result buffer, ADC converter for Synchronize conversion and other variables which are used for synchronized conversions.
Iopt_Adc_StopSyncBuffer
  This interface stops the running synchronize conversion and resets the used resources.
Iopt_Adc_SyncGetStreamLastPointer
  This interface returns two values, number of valid samples stored in the result buffer and the pointer to latest results. In circular buffer when the number of samples exceeds the buffer size, the maximum buffer size is returned.

## Slide 30: ADC Driver APIs (AUTOSAR R4.3)
Function | Explanation | Deviation to AUTOSAR
Adc_Init (Iopt_Adc_Init) | This function initializes the ADC driver with the configuration structure which specifies the required configuration of the ADC driver. It initializes autoscan, software trigger, hardware trigger, sync trigger and streaming trigger conversion modes if they are configured. | -
Adc_DeInit (Iopt_Adc_Shutdown) | This function stops all ADC driver activity on all configured devices and resets the used hardware. | Adc_DeInit can be called irrespective of any group state as ADC group status is not implemented.

## Slide 31: ADC Driver APIs (AUTOSAR R4.3)
Function | Explanation | Deviation to AUTOSAR
Adc_SetupResultBuffer (Iopt_Adc_SetupResultBuffer) | This interface is used to initialize the result buffer pointer of the selected conversion group with the address value passed as parameter. | Adc_SetupResultBuffer initializes the result buffer pointer of the selected conversion group with the address value passed as parameter only for streaming conversion group.
Adc_GetStream LastPointer (Iopt_Adc_GetStreamLastPointer) | This interface is used to set the pointer, passed as parameter (PtrToSamplePtr) to point to the ADC result buffer to the oldest conversion, where the result was not yet read. | Returns the number of valid samples per channel only for streaming group conversion. Pointer to the address of the oldest conversion element not yet read. ADC_RESULT_ALIGNMENT is the natural alignment coming from the HW. Group status is not implemented with - call during ADC_BUSY returns NULL. - No state transition trigger for group status. - No guarantee for consistency.

## Slide 32: ADC Driver APIs (AUTOSAR R4.3)
Function | Explanation | Deviation to AUTOSAR
Adc_EnableGroupNotification (Iopt_Adc_EnableGroupNotification(Group,1)) | The interface is used to enable the notification mechanism for the requested ADC channel conversion group. | -
Adc_DisableGroupNotification (Iopt_Adc_DisableGroupNotification (Group,0)) | The interface is used to disable the notification mechanism for the requested ADC channel conversion group. | -

## Slide 33: ADC Driver APIs (AUTOSAR R4.3)
Function | Explanation | Deviation to AUTOSAR
Adc_EnableHardwareTrigger (Iopt_Adc_EnableHwTrigger(Group,1)) | This interface is used to enable the hardware trigger for the requested ADC channel conversion group. | The following requirement is not implemented: “The function Adc_EnableHardwareTrigger shall reset the internal group result buffer pointer, that conversion result storage always starts, after calling Adc_EnableHardwareTrigger, at the result buffer base address which was configured with Adc_SetupResultBuffer”.
Adc_DisableHardware Trigger (Iopt_Adc_EnableHwTrigger(Group,0)) | This interface is used to disable the hardware trigger for the requested ADC channel conversion group. | Adc_DisableHardwareTrigger does not set the group status to state ADC_IDLE as ADC group status is not implemented.

## Slide 34: ADC Driver APIs (AUTOSAR R4.3)
Function | Explanation | Deviation to AUTOSAR
Adc_StartGroupConversion | This interface is used to start the conversion of all channels of the requested ADC Channel conversion group. Only for groups configured with software trigger source. | Conversion result storage starts from the first address of the internal buffer. (The result buffer base address set by Adc_SetupResultBuffer() can be used only for streaming conversion channels.)
Adc_ReadGroup | Reads group conversion result of the last completed conversion round. | DSADC: ADC_RESULT_ALIGNMENT is the natural alignment coming from the HW. VADC: ADC_RESULT_ALIGNMENT is right aligned and not configurable. Calling Adc_ReadGroup does not trigger the required state transition as ADC Group Status is not implemented.
Can not be used for streaming conversion groups
!

## Slide 35
Deviations of functional requirements
  No service is provided to stop running conversion of a SwTrigger Group
  No service is provided to get the ConverterGroup Status
  Adc_GetStreamLastPointer() service can only be used for streaming conversion (burst)
  Limit checking feature for HwTrigger is not implemented (yet). Channel specific limit checking is only implemented for fast compare channels
  ADC channels can be assigned to more than one group with some limitations. Please refer the DIM for Iopt_Adc for limitations and constraints
ADC Driver APIs (AUTOSAR R4.3)

## Slide 36: IOPT_ADC Driver APIs - DSADC
Iopt_Adc_DsEnableFilter
  This operation enables or disables different configuration parameters of main or comb filter. This interface can also reset main or comb filter. If the user does not pass correct command (or no command) for the given filter parameter, then this interface makes that filter parameter to the reset value.
Iopt_Adc_DsSetGain
  This operation sets the gain factor of a DSADC channel. Gain factor of analog input path can be set to 1, 2 or 4.
Iopt_Adc_DsGetStreamLastPointer
  This interface returns two values, number of valid samples available to copy from the time when last read happened and the pointer to the latest result. After each call of this interface, the pointer and result count are reset to the new values. In case of circular buffer, when the number of samples has exceeded the buffer size, the maximum buffer size is returned.

## Slide 37: IOPT_ADC Driver APIs - DSADC
Iopt_Adc_DsSetUpResultBuffer
  This interface prepares the external result buffer where the conversion results will be stored. This interface must be called each time before calling the Iopt_Adc_DsEnableHardwareTrigger interface.
Iopt_Adc_DsEnableHardwareTrigger
  This interface enables the DSADC module to store result data inside the external user buffer and it also enables the used DMA or INT resources.
Iopt_Adc_DsDisableHardwareTrigger
  This interface disables the DSADC module to store result data inside the external user buffer and it also disables the used DMA or INT resources.
Iopt_Adc_DsEnableGroupNotification
  This operation enables or disables the activation of the notification at a completed group conversions. This interface must be called before starting the conversion. This operation can be used with hardware trigger with streaming linear buffer. When the buffer is full, notification is generated for the user function. External linear buffer mode supports only the notification mechanism, whereas the external circular buffer mode does not support it.

## Slide 38: IOPT_ADC Driver APIs - DSADC
Iopt_Adc_DsCalibrateDevice
  This interface is used to calibrate the DSADC converter due to change in the temperature or other conditions which affects DSADC normal operation. The user must make sure that the conversions are not requested when the calibration is running.
Iopt_Adc_DsGetCalibStatus
  The user can poll current status of calibration of needed converter with this interface. This interface returns the calibration status as uncalibrated, running, calibrated or terminated for the given converter.
Iopt_Adc_DsActivateDevice
  This interface activates or deactivates a particular converter. This operation can also be used to activate or deactivate more than one converter at the same time when synchronized operation is required.

## Slide 39
Agenda
Functional Description & Features
1
APIs
2
Integration Highlights
3
Configuration
4
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
HW Resources
6
Constraints & Limitations
7

## Slide 40: ADC Driver - VADC Integration Highlights
Software trigger mode
  One interrupt channel is needed for each conversion group
Hardware trigger mode and streaming mode
  One DMA channel per conversion group
  Three interrupt channels per conversion group
    Service request handling of VADC conversion group (to trigger DMA after conversion)
    DMA transaction finished (resetting DMA, call user notification)
Sync trigger mode
  1 + x interrupt channels per Sync “Family”
    Service request handling of VADC master and each slave (to trigger DMA after conversion)
General
  One PWM channel per trigger has to be configured if the GTM is used as trigger
  PORT channel configuration is needed for using GPIO pins as trigger

## Slide 41: ADC Driver - DSADC Integration Highlights
Hardware trigger streaming mode
  One DMA channel per channel.
  Two interrupt channels per DSADC channel, one for service request handling of the DSADC and another for the DMA after copying the results from the registers to the result buffer.

## Slide 42
Agenda
Functional Description & Features
1
APIs
2
Integration Highlights
3
Configuration
4
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
HW Resources
6
Constraints & Limitations
7

## Slide 43: ADC Driver - VADC Configuration
General configuration structure
  Display the class type along with the Object

## Slide 44: ADC Driver - VADC Configuration - AdcConfigSet

## Slide 45: ADC Driver - VADC Configuration - AdcHwUnit

## Slide 46: ADC Driver - VADC Configuration - AutoscanGroup

## Slide 47: ADC Driver - VADC Configuration - AdcChannel

## Slide 48: ADC Driver - VADC Configuration - EmuxGroup

## Slide 49: ADC Driver - VADC Configuration - SyncMasterGroup

## Slide 50: ADC Driver - VADC Configuration - SyncSlaveGroup

## Slide 51: ADC Driver - VADC Configuration - FastCompare

## Slide 52: ADC Driver Configuration Example - DSADC module
Configuration
General configuration structure

## Slide 53: ADC Driver Configuration Example - DSADC module
Converter

## Slide 54: ADC Driver Configuration Example - DSADC module
Modulator

## Slide 55: ADC Driver Configuration Example - DSADC module
Demodulator

## Slide 56: ADC Driver Configuration Example - DSADC module
Integrator

## Slide 57: ADC Driver Configuration Example - DSADC module
Filter

## Slide 58: ADC Driver Configuration Example - DSADC module
Calibration

## Slide 59: ADC Driver Configuration Example - DSADC module
DsadcChannel

## Slide 60
Agenda
Functional Description & Features
1
APIs
2
Integration Highlights
3
Configuration
4
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
HW Resources
6
Constraints & Limitations
7

## Slide 61: ADC Driver Dependencies
IOPT_CORE
use

## Slide 62
Agenda
Functional Description & Features
1
APIs
2
Integration Highlights
3
Configuration
4
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
HW Resources
6
Constraints & Limitations
7

## Slide 63
ADC Driver Hardware Resources

## Slide 64
Agenda
Functional Description & Features
1
2
APIs
2
6
Integration Highlights
3
8
Configuration
4
10
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
13
HW Resources
6
15
Constraints & Limitations
7
17

## Slide 65: ADC Driver - VADC Constraints & Limitations
Max three of four trigger groups per Hardware Unit (HwUnit)
  AutoScan
  Software Trigger (SwTrigger)
  Hardware Trigger (HwTrigger)
  Synchronized Trigger (Master / Slave)
Either master or slave sync. group can be configured on a single hardware unit.
The external result buffer (streaming buffer) must be
  associated with ASIL_C safety level
  accessible by DMA (RessourcePatition)

## Slide 66: ADC Driver - DSADC Constraints & Limitations
Either hardware or software
The external result buffer must have ASIL_C safety class level for the buffer allocation and the buffer memory must accessible by DMA. The DMA driver integration manual provides more details about the DMA buffer allocation.

## Slide 67: Thank You
?
Please Feel Free To Ask Questions