## Slide 1: DIO Driver Training Slides
ECU17
www.continental-corporation.com
Rev. 1.0 / 09-Aug-2018 / P ES SE EEA BSWP

## Slide 2
Agenda
Functional Description & Features
1
2
APIs
2
6
Integration Highlights
3
8
Configuration
4
10
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
13
HW Resources
6
15
Constraints & Limitations
7
17

## Slide 3: Functional Description & Features
The generic DIO functionality handles the microcontroller's pins (e.g. PORT or MSC) and ASIC pins. The driver is able to read the logical level or physical state of a pin and to control the logical level or physical state of an output pin.
All processor resources are covered which are able to perform the DIO functionality for setting or getting the state or level.

## Slide 4
Agenda
Functional Description & Features
1
2
APIs
2
6
Integration Highlights
3
8
Configuration
4
10
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
13
HW Resources
6
15
Constraints & Limitations
7
17

## Slide 5: APIs
Iopt_Dio_Init - It initializes the given configuration instance.
Iopt_Dio_SetOutput - It sets the logical level or physical state of the given DIO channel
Iopt_Dio_GetOutput - It gets the logical level or physical state of the given DIO channel
Iopt_Dio_ReadChannelGroup- It reads a subset of the adjoining bits of a port, as an LSB aligned value.
Iopt_Dio_WriteChannelGroup- It sets a subset of the adjoining bits of a port to a specified level, without changing the remaining channels of the port and the channels configured as input.
Iopt_Dio_ReadPort- It reads the level of all channels of a port.
Iopt_Dio_WritePort- It sets the level of all channels of a port.
Iopt_Dio_FlipChannel- It flips the level of a channel (change from 1 to 0 or from 0 to 1).

## Slide 6
Agenda
Functional Description & Features
1
2
APIs
2
6
Integration Highlights
3
8
Configuration
4
10
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
13
HW Resources
6
15
Constraints & Limitations
7
17

## Slide 7: Integration Highlights
DIO driver is dependent on MSC and ASIC configurations if these pins are controlled via DIO operations.

## Slide 8
Agenda
Functional Description & Features
1
2
APIs
2
6
Integration Highlights
3
8
Configuration
4
10
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
13
HW Resources
6
15
Constraints & Limitations
7
17

## Slide 9: Configuration Structure

## Slide 10: Configuration Example
Port pin
MSC Channel

## Slide 11: Configuration Example
ASIC Channel
ASIC channel parallel control over MSC channel.

## Slide 12: Configuration Example
ASIC channel parallel control over PORT channel.

## Slide 13: Configuration Example
Access to all pins of same Port peripheral
DioChannelGroup

## Slide 14
Agenda
Functional Description & Features
1
2
APIs
2
6
Integration Highlights
3
8
Configuration
4
10
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
13
HW Resources
6
15
Constraints & Limitations
7
17

## Slide 15: Dependencies

## Slide 16
Agenda
Functional Description & Features
1
2
APIs
2
6
Integration Highlights
3
8
Configuration
4
10
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
13
HW Resources
6
15
Constraints & Limitations
7
17

## Slide 17: HW Resources
General Purpose I/O Ports and Peripheral I/O Lines (Ports)
MSC and ASIC input/output channel

## Slide 18
Agenda
Functional Description & Features
1
2
APIs
2
6
Integration Highlights
3
8
Configuration
4
10
Configuration Structure
4.1
Configuration Example
4.2
Dependencies
5
13
HW Resources
6
15
Constraints & Limitations
7
17

## Slide 19: Constraints & Limitations
Check microcontroller manual for available port channels which can be used for DIO application.
PORT/MSC/ASIC channels need to be configured in the respective drivers before they are used by DIO operations. All dependent drivers must be initialized before DIO driver.
MSC and ASIC pre-process should be called before DIO pre-process if they are controlled by DIO.

## Slide 20: Document History
Revision | Changes | Valid for
1.0 | First version for ECU17 | DIO_1.3.0